## Slide 1: A classification of the different types of HME heat sources
Frank Ballarano – Erick Braquet – Cyril Calatrava – Philippe Koehl Jacques Ruer*
IWAHLM15 - Assisi – September 2022
The CleanHME project has received funding from the European Union’s Horizon2020 research and innovation programme under grant agreement no 951974

## Slide 2
September 2022 IWAHLM15 - Assisi
Assumption: HME is a reactor that generates heat
HME Heat source

## Slide 3
Assumptions:
  HME heat may supply a thermodynamic converter
  The converter may generate electricity
HME Heat source
September 2022 IWAHLM15 - Assisi

## Slide 4
Assumptions:
  HME heat may supply a thermodynamic converter
  The converter may generate electricity
HME Heat source
feedback
  Feedback possible
September 2022 IWAHLM15 - Assisi

## Slide 5
Types of HME heat sources
TYPE 1 : Excitation energies include some heat
TYPE 2 : Excitation does not include heat
TYPE 3 : Self-sustained system – production of electricity exceeds excitation consumption
TYPE 4: Solid state technology self-sustained (not discussed further here)
The following classification will probably be temporary, as explained below
September 2022 IWAHLM15 - Assisi

## Slide 6
Electrical energy input for :
heating + supply for high exergy excitation
Type 1 – Heating + Excitation
September 2022 IWAHLM15 - Assisi

## Slide 7
Electrical energy input for :
heating + supply for high exergy excitation
Type 1 – Heating + Excitation
September 2022 IWAHLM15 - Assisi
High exergy = Any form of energy other than heat

## Slide 8
Heating + Exergy Excitation
September 2022 IWAHLM15 - Assisi
Why make a distinction between heating and exergy excitation ?

## Slide 9
Heating + Exergy Excitation
September 2022 IWAHLM15 - Assisi
Why make a distinction between heating and exergy excitation ?
It is a problem of power control

## Slide 10
Heating + Exergy Excitation
September 2022 IWAHLM15 - Assisi
If the excitation is only heat you must control the cooling carefully

## Slide 11
Heating + Exergy Excitation
September 2022 IWAHLM15 - Assisi
If the excitation is only heat you must control the cooling carefully
If you don’t you risk a runaway !

## Slide 12
Heating + Exergy Excitation
September 2022 IWAHLM15 - Assisi
Cooling method for stable operation if the excitation is only heat
Reaction is controlled by adjusting the coolant temperature
Heat flow
Temperature
HME Operating point
Heat is recovered at this temperature
HME power curve
Cooling power curve
DT

## Slide 13
Heating + Exergy Excitation
September 2022 IWAHLM15 - Assisi
If the excitation includes some exergy there is an additional method to control the power

## Slide 14
Electrical energy input for :
heating + supply for high exergy excitation
DEFINITIONS:
Excess Heat = Heat output – Energies input to the reactor
Coefficient of Performance =
Heat output / Electricity to excitation supply unit
Amplification factor =
Heat surplus output /Supply of high exergy excitation
Type 1 – Heating + Excitation
September 2022 IWAHLM15 - Assisi

## Slide 15
Excess Heat = Not changed by insulation
Amplification factor = Not changed by insulation
Coefficient of Performance = changed by insulation
From Type 1 to Type 2
September 2022 IWAHLM15 - Assisi
Good thermal insulation
Low thermal insulation

## Slide 16
Excess Heat = Not changed by insulation
Amplification factor = Not changed by insulation
Coefficient of Performance = changed by insulation
COP is not the relevant metrics
AMPLIFICATION FACTOR and
EXCESS HEAT SPECIFIC ENERGY (W/kg)
should be preferred to evaluate the performance of a HME reactor
September 2022 IWAHLM15 - Assisi
From Type 1 to Type 2

## Slide 17
Excess Heat = heat loss + heat export
Useful heat exported for uses
Heat loss may be recovered for other uses
Type 2 : Heat export
September 2022 IWAHLM15 - Assisi

## Slide 18
The difference is linked to the relative importance of the heat losses compared to heat generation
Difference between Type 1 and Type 2
September 2022 IWAHLM15 - Assisi
Small reactor
Heat loss > Internal heat flux
Type 1
Large reactor
Heat loss < Internal heat flux
Type 2

## Slide 19
The difference is linked to the relative importance of the heat losses compared to heat generation
Difference between Type 1 and Type 2
September 2022 IWAHLM15 - Assisi
Small reactor
Heat loss > Internal heat flux
Type 1
Large reactor
Heat loss < Internal heat flux
Type 2

## Slide 20
The difference is linked to the relative importance of the heat losses compared to heat generation and to the size of the reactor
Difference between Type 1 and Type 2
September 2022 IWAHLM15 - Assisi
Single laboratory cell
Industrial cluster of cells

## Slide 21
Heat transferred to a thermodynamic heat converter
Production of some electricity
Coupling HME + Converter
September 2022 IWAHLM15 - Assisi

## Slide 22
Heat transferred to a thermodynamic heat converter
Production of some electricity
TYPE 2 :
Electricity production < excitation consumption
TYPE 2 HME + Converter
September 2022 IWAHLM15 - Assisi

## Slide 23
Heat transferred to a thermodynamic heat converter
Production of some electricity
TYPE 2 :
Electricity production < excitation consumption
TYPE 2 HME + Converter
Elec.
HEAT
September 2022 IWAHLM15 - Assisi

## Slide 24
TYPE 3 :
Electricity production > excitation consumption
Export of electrical energy
Export of heat: engine losses + insulation losses
TYPE 3 : Self-sustained
September 2022 IWAHLM15 - Assisi

## Slide 25
TYPE 3 :
Electricity production > excitation consumption
Export of electrical energy
Export of heat: engine losses + insulation losses
TYPE 3 : Self-sustained
Elec.
+
Heat
September 2022 IWAHLM15 - Assisi

## Slide 26
Condition for self-sustained operation
(HEAT OUTPUT – HEAT LOSS)
X
CONVERSION EFFICIENCY (h) -----------------------------------
> EXCITATION ENERGY INPUT
September 2022 IWAHLM15 - Assisi

## Slide 27
Thermal engines transform the heat into mechanical power
Conversion efficiency limited by Carnot’s law:
hc = (1 – Tcold / Thot)
Conversion efficiency of an engine: h = hr x hc
hr : Relative efficiency
TYPE 3 involves thermodynamic converters
September 2022 IWAHLM15 - Assisi

## Slide 28
Thermodynamic converters
Ericsson engine - - - - - - - - - - - - - - - - - - - - - - - 0.70
Stirling engine - - - - - - - - - - - - - - - - - - - - - - - - 0.60
Steam turbine - - - - - - - - - - - - - - - - - - - - - - - 0.65
Organic Rankine Cycles - - - - - - - - - - - - - - - - - 0.50
Thermoelectric converters - - - - - - - - - - - - - - - 0.30
Johnson thermo-electrochemical converters - - 0.70
hr : Relative efficiencies (typical)
September 2022 IWAHLM15 - Assisi

## Slide 29
Conversion efficiencies
September 2022 IWAHLM15 - Assisi

## Slide 30
Converters applicability
September 2022 IWAHLM15 - Assisi

## Slide 31
Theoretical minimum COP for transition from TYPE 2 to TYPE 3
(Tcold = 300K – No heat loss – Perfect excitation supply)
Influence of conversion efficiency on self-sustained operation
September 2022 IWAHLM15 - Assisi

## Slide 32
The distinction between Type 1 and Type 2 will only last during the development period of the devices (laboratory setups)
All useful heat sources will be at least Type 2
The distinction between Type 2 and type 3 is given by the output: HEAT or ELECTRICITY
Conclusion: Simplified classification
September 2022 IWAHLM15 - Assisi
It is proposed to use a simplified classification that would remain meaningful in the future:
HME Heat Sources  HME-HS
HME Power Sources  HME-PS

## Slide 33: Thank you for your attention

## Slide 34: Thank you! Any questions?
The CleanHME project has received funding from the European Union’s Horizon2020 research and innovation programme under grant agreement no 951974
This work reflects only the author's view and the European Commission is not responsible for any use that may be made of the information it contains.