## Slide 1: A technological foresight for the future deployment of different types of HME energy sources
Frank Ballarano – Erick Braquet – Cyril Calatrava – Philippe Koehl Jacques Ruer*
IWAHLM15 - Assisi – September 2022
The CleanHME project has received funding from the European Union’s Horizon2020 research and innovation programme under grant agreement no 951974

## Slide 2
Assumption: HME reactor that generates heat
HME Heat source
What can we do with it ?
What are the uses of heat that
could benefit from HME ?
Study included as one CleanHME task
First part of the study : What are the
present uses of heat
September 2022
IWAHLM15 – Assisi

## Slide 3
September 2022
IWAHLM15 – Assisi
HME is a new source of heat
Source of energy
HEAT
Use of the heat
HME reactors may displace:
Combustion of fossil fuels
Nuclear reactors
Solar collectors
Electrical heating

## Slide 4
September 2022
IWAHLM15 – Assisi
Direct and indirect use of heat
Source of energy
HEAT
Use of the heat
Source of energy
HEAT
Conversion in another entity
Use of the entity
DIRECT USE OF HEAT
INDIRECT USE OF HEAT

## Slide 5
September 2022
IWAHLM15 – Assisi
Examples of direct use of heat
Source of energy
HEAT
Use of the heat
Space heating
Metal melting
Distillation
Etc..

## Slide 6
September 2022
IWAHLM15 – Assisi
Examples of indirect use of heat
Source of energy
HEAT
Conversion in another entity
Use of the entity
Internal Combustion Engine  Mobility
Metal foundry  Metallic goods
Steam turbine  Electricity
Etc..
DIRECT or INDIRECT depend on the point of view

## Slide 7
September 2022
IWAHLM15 – Assisi
Direct and indirect use of heat
Source of energy
HEAT
Use of the heat
Source of energy
HEAT
Conversion in another entity
Use of the entity
DIRECT USE OF HEAT
INDIRECT USE OF HEAT
WE MUST CONSIDER BOTH
HME
HME

## Slide 8
September 2022
IWAHLM15 – Assisi
Information desired:
  Type of uses – Number of users in the world at the different temperature levels and power levels – power density –
Source of information:
  Statistics from governments and institutions (EU – DOE – IEA – national bodies)
  Statistics from particular professional organisations (BP World review – Oil & Gas Refineries – Cement – Iron & Steel – Pulp & paper – etc…)
  Review of the literature
Investigation of the present heat uses

## Slide 9
September 2022
IWAHLM15 – Assisi
First remarks:
  No sources give the information required directly
  Different studies use different reference frames to describe the industry
  Studies dating from a few years ago must be reanalysed to take the evolution into account
  Statistics for EU28 and EU27 make comparison difficult in Europe
  Recent economic situation (COVID) complicates the reanalysis – reference year : 2019 or 2020
Investigation of the present heat uses

## Slide 10
September 2022
IWAHLM15 – Assisi
Difficulties:
  A major source of statistical data are devoted to the consumption of the fossil fuels or the emissions of CO2
  Coherence with other sources of information is not always observed
  Data for residential and commercial sectors are only meaningful in OECD countries
  Different units (Quadrillion Btu – EJ – PJ – Mtoe – MWh – etc..)
Investigation of the present heat uses

## Slide 11
September 2022
IWAHLM15 – Assisi
Some careful analysis is requested. For examples:
  Iron production in blast furnace: Not all the coal and coke consumed should be accounted as energy because some carbon is used for iron ore reduction
  Aluminium industry: Production of alumina uses heat at low temperature (Bayer process) and at high temperature (alumina firing) while production of aluminium uses electricity
  Power stations electricity output is not heat input
  Etc…
Investigation of the present heat uses

## Slide 12
September 2022
IWAHLM15 – Assisi
Methodology :
  Necessity to simplify the data collected especially for the industrial uses
  Extrapolations are used to translate regional data into global data – this introduces distortion and inaccuracies
  Introduction of average users for the different categories – the number of users can only be approximated
  Future trends are not considered for the moment but will be in the continuation of the study if justified
Investigation of the present heat uses

## Slide 13
September 2022
IWAHLM15 – Assisi
Investigation of the present heat uses
EXAMPLE : EUROSTAT – Energy data – 2020 edition

## Slide 14
September 2022
IWAHLM15 – Assisi
Investigation of the present heat uses
EUROSTAT – Energy data – 2020 edition
Residential :
How many appliances and devices ?
EU 28:
6400kWh/a per capita
USA :
11000kWh/a per capita
MANY COUNTRIES:
Much less

## Slide 15
PJ (1015J) | Low temperature (<100°C- | Medium temperature (100°C – 400°C) | High temperature (>400°C) | Sum | Energy intensive industries
Iron and Steel | 50 | 53 | 1044 | 1147 | 1147
Non-ferrous metals | 10 | 5 | 98 | 113 | 113
Chemicals | 351 | 180 | 346 | 877 | 877
Mineral products | 57 | 53 | 826 | 936 | 936
Ore extraction | 7 | 5 |  | 12 | 
Food and beverages | 256 | 162 |  | 418 | 418
Textile | 23 | 36 | 13 | 72 | 
Paper | 175 | 246 | 92 | 513 | 513
Transport equipment | 29 | 10 | 4 | 43 | 
Machinery | 67 | 22 | 10 | 99 | 
Other industries | 119 | 58 | 29 | 206 | 
TOTAL (PJ/a) | 1144 | 830 | 2462 | 4436 | 4004
Total Mtoe/a | 27,32 | 19,82 | 58,8 | 105,94 | 
September 2022
IWAHLM15 – Assisi
Industrial uses of heat :
Energy-intensive sectors
Industry analysis: limited to energy-intensive industries
Energy-intensive = 90% of total
Quantification of the European industrial heat demand by branch and temperature level
Tobias Naegler*,†, Sonja Simon, Martin Klein and Hans Christian Gils
INTERNATIONAL JOURNAL OF ENERGY RESEARCH Int. J. Energy Res. 2015; 39:2019–2030

## Slide 16
September 2022
IWAHLM15 – Assisi
World uses of heat
Estimates of number of users per sector
Estimations only !
Industry: Only selected energy-intensive sectors
(Many industries missing)
Residential and commercial: extrapolations from EU or OECD statistics

## Slide 17
September 2022
IWAHLM15 – Assisi
Overview of Heat Users

## Slide 18
September 2022
IWAHLM15 – Assisi
Overview of Heat Users
Linear scale
Residential appliances
Cars

## Slide 19
September 2022
IWAHLM15 – Assisi
Overview of Heat Users

## Slide 20
September 2022
IWAHLM15 – Assisi
Overview of Heat Users
Logarithmic scale
1 400 000 000 automobiles
440
Nuclear reactors
Power levels, typical temperatures and numbers of users are only indicative

## Slide 21
September 2022
IWAHLM15 – Assisi
Cumulated installed power per sector
Cumulated powers - Logarithmic scale

## Slide 22
September 2022
IWAHLM15 – Assisi
Cumulated installed power per sector
Cumulated powers - Linear scale
7.2 E7

## Slide 23
September 2022
IWAHLM15 – Assisi
Cumulated HEAT consumed per sector
Cumulated energies - Logarithmic scale

## Slide 24
September 2022
IWAHLM15 – Assisi
Introduction of 100°C Class HME
100°C sources : huge market for residential and commercial uses

## Slide 25
September 2022
IWAHLM15 – Assisi
Introduction of 350°C Class HME
200°C to 350°C sources : large market for industrial boilers

## Slide 26
September 2022
IWAHLM15 – Assisi
Introduction of HME Generators
350°C+ sources : Heat conversion in electricity

## Slide 27
IWAHLM15 – Assisi
HME generators replace power stations
September 2022
350°C+ sources : All power stations progressively displaced

## Slide 28
September 2022
IWAHLM15 – Assisi
HME generators can supply all users
350°C+ sources : Industrial uses of fossil fuels progressively displaced

## Slide 29
September 2022
IWAHLM15 – Assisi
What about mobility ?
Internal Combustion Engines and Aircraft Engines : Indirect use – heat conversion
Fossil fuels offer a unique high specific energy density
Road
Marine
Air

## Slide 30
September 2022
IWAHLM15 – Assisi
What about mobility ?
Internal Combustion Engines and Aircraft Engines : Indirect use – heat conversion
Fossil fuels offer a unique high specific energy density
Road
Marine
Air
Mobile equipment :
Difficult to supply the heat that is used indirectly
Necessity of high power density (> 1kW/liter)
May be satisfied indirectly:
Electricity for recharge of electric vehicles
Supply of hydrogen
Synthetic fuels via H2 and CO2 (Direct Air Capture)

## Slide 31
September 2022
IWAHLM15 – Assisi
What about mobility ?
Hydrogen refuelling station in Mountain View : The future?

## Slide 32
September 2022
IWAHLM15 – Assisi
What about mobility ?
Hydrogen refuelling station in Mountain View : The future?

## Slide 33
Addressable market
HME temperature: | < 100°C | <200°C | < 300°C | > 300°C
HME HEAT SOURCES | Residential heating x 109 units kW | Commercial & industrial heating x 106 units 100S kW |  | 
HME HEAT SOURCES | Residential heating x 108 units Several kW | Low pressure Boilers x 106 units 100S kW -MW | High pressure boilers x 105 units 100S kW -MW | Process heat x 104 units 100S kW -MW
HME GENERATORS |  | Autonomous systems x 106 units 100S kW -MW | Steam turbines x 105 units 100S kW -MW | Power generators x 109 units kW - MW
SOLID STATE | Future developments |  |  | 
September 2022
IWAHLM15 – Assisi

## Slide 34
HME temperature: | < 100°C | <200°C | < 300°C | > 300°C
HME HEAT SOURCES | Residential heating x 109 units kW | Commercial & industrial heating x 106 units 100S kW |  | 
HME HEAT SOURCES | Residential heating x 108 units Several kW | Low pressure Boilers x 106 units 100S kW -MW | High pressure boilers x 105 units 100S kW -MW | Process heat x 104 units 100S kW -MW
HME GENERATORS |  | Autonomous systems x 106 units 100S kW -MW | Steam turbines x 105 units 100S kW -MW | Power generators x 109 units kW - MW
SOLID STATE | Future developments |  |  | 
Prime market
September 2022
IWAHLM15 – Assisi

## Slide 35
HME temperature: | < 100°C | <200°C | < 300°C | > 300°C
HME HEAT SOURCES | Residential heating x 109 units kW | Commercial & industrial heating x 106 units 100S kW |  | 
HME HEAT SOURCES | Residential heating x 108 units Several kW | Low pressure Boilers x 106 units 100S kW -MW | High pressure boilers x 105 units 100S kW -MW | Process heat x 104 units 100S kW -MW
HME GENERATORS |  | Autonomous systems x 106 units 100S kW -MW | Steam turbines x 105 units 100S kW -MW | Power generators x 109 units kW - MW
SOLID STATE | Future developments |  |  | 
Learning curve
September 2022
IWAHLM15 – Assisi

## Slide 36
HME temperature: | < 100°C | <200°C | < 300°C | > 300°C
HME HEAT SOURCES | Residential heating x 109 units kW | Commercial & industrial heating x 106 units 100S kW |  | 
HME HEAT SOURCES | Residential heating x 108 units Several kW | Low pressure Boilers x 106 units 100S kW -MW | High pressure boilers x 105 units 100S kW -MW | Process heat x 104 units 100S kW -MW
HME GENERATORS |  | Autonomous systems x 106 units 100S kW -MW | Steam turbines x 105 units 100S kW -MW | Power generators x 109 units kW - MW
SOLID STATE | Future developments |  |  | 
Major market : Electrical generators
September 2022
IWAHLM15 – Assisi

## Slide 37
September 2022
IWAHLM15 – Assisi
Evaluate the HME potential development once the characteristics of the reactors are better defined
Examine the technological gaps for the development
Consider the ongoing energy transition and the competition of renewable energies
Next steps of the study

## Slide 38
As we are nearing the launch of applications it is now time to remember that there are always several solutions to a problem
HME will not conquer a virgin World but will face competition in many sectors.
HME will be adopted only where it is better than other existing options
September 2022
IWAHLM15 – Assisi
The end of our Golden Age
Jean-Auguste-Dominique Ingres - L'Âge d'or, 1862, - Fogg Art Museum, Cambridge

## Slide 39
As we are nearing the launch of applications it is now time to remember that there are always several solutions to a problem
HME will not conquer a virgin World but will face competition in many sectors.
HME will be adopted only where it is better than other existing options
September 2022
IWAHLM15 – Assisi
The end of our Golden Age

## Slide 40
September 2022
IWAHLM15 – Assisi
Electricity
HEAT
Use of the heat
HME reactor
Competition ahead ? : An example

## Slide 41
September 2022
IWAHLM15 – Assisi
Electricity
HEAT
Use of the heat
HME reactor
Competition ahead ? : An example
Heat Pump

## Slide 42
September 2022
IWAHLM15 – Assisi
Competition ahead ? :
Example : Heat Pumps

## Slide 43
HME heat sources may find a large use for space heating and water heating – Many units with low thermal power
The learning curve will give access to larger units and higher temperatures
Development of large units will open the market for industrial boilers
HME electricity generators will find applications at all scales of power
Transportation requires high HME specific power – May be accessed indirectly via the synthesis of fuels, with no modification of the existing engines and energy distribution infrastructure
Competition will exist
CONCLUSIONS
September 2022
IWAHLM15 – Assisi

## Slide 44: Thank you! Any questions?
The CleanHME project has received funding from the European Union’s Horizon2020 research and innovation programme under grant agreement no 951974
This work reflects only the author's view and the European Commission is not responsible for any use that may be made of the information it contains.